## Slide 1: Digital Logic and Design

## Slide 2
https://github.com/sajjo79/Digital-Logic-Design
Slides can be found at

## Slide 3: Storage Elements: D Latch
Chapter 4: Sequential circuits

## Slide 4: Background
NOR gates based SR Latch may have following three states:
  Set State: S=1, R=0
  Stable State: S=0, R=0
  Reset State: S=0, R=1
  Forbidden State: S=1, R=1
We want to avoid this forbidden state that introduces instability in the circuit

## Slide 5: D Latch (Transparent Latch)
To eliminate the forbidden state, ensure that both S and R will not be equal to 1 at the same time
D-Latch (data latch) puts this restriction on SR Latch.
  This has only two inputs D and En
  D input goes to the S input
  D’ input goes to R input
  If En = 0: S=R=1. circuit is disabled and its state is not changeable.
  If En = 1:
    D=0: S=0, R=1, Circuit reaches reset state
    D=1: S=1, R=0, Circuit reaches set state

## Slide 6: The D-Latch
It is suitable to store binary information (BI)
BI at D is transferred to Q output as shown in the table. This is why it is called transparent latch
Graphic symbols for the various latches

## Slide 7
7
Thanks for watching
Dr. Sajid Iqbal
Assistant Professor
Department of Computer Science
Bahauddin Zakariya University, Multan
Allah Hafiz
Slides are available at: https://github.com/sajjo79/Digital-Logic-Design